## Slide 1: “How to keep predators, particularly honey badgers, away from the fence and the penguins??”
Group 31

## Slide 2: INSIGHT FROM THE LITERATURE
1. The world’s most fearless animal
2. Courageous, aggressive, strong and
SMART!!
Weaknesses:
Nocturnal
Heavily rely on smell for hunting
Repelled by certain scents e.g Citronella oil, garlic, vinegar etc

## Slide 3: Proposed solution: Honey Badger Repellent System
Light and scent as a repellent
Periodically spray the vicinity to desensitize the colony
Once animal detected – turn on the strobing lights and power the spray

## Slide 4: Overview
Overview of System

## Slide 5: Animal Detection Subsystem
Light sensor
*Power efficiency
*Increases electronics’ lifespan
Passive Infrared (PIR)
*Common use in literature
*Long-range detection
IR Break beam sensor
* Short-range detection
Light sensor
PIR sensor
IR Break beam
ANIMAL DETECTED!!
Sequential logic of operation:

## Slide 6: Networking and User Interface Subsystem

## Slide 7: Overview
Human is the classifier, not machine learning
UI must minimize
human error
No machine learning
No database
Native web-application
Overall System Architecture

## Slide 8: Main Goal is Reliability, Because Consequences are Severe
Drivers of Failure:
ESP32-cam suffers from frequent
camera malfunctions
Wireless communication fails a lot
User's fail a lot, especially with bad UI

## Slide 9: Networking

## Slide 10: Networking Design
Application Layer Design
Correct Server Architecture
Concurrency Issues
Control signals vs data signals
TCP and UDP
Message Structure and Protocol Design
Server Architecture

## Slide 11: Peer-to-peer Network
Each ESP32-cam is BOTH A SERVER AND A CLIENT in this architecture
Effectiveness scales with number of detection devices
Peer-to-peer architecture

## Slide 12: User-Interface

## Slide 13: User-Interface Design: Idle
User-interface in Idle Mode

## Slide 14: Detection Event and Registered Devices
Detection Alert
Registered Devices

## Slide 15: System Log and Camera Broken Handling
Data written for broken camera event, in a textfile
System Log